# Update:  9/04/03

# TP77350 Issue “M”- 85 QUESTION TEST

# Please fill out completely.

# Name:________________________________________________________

QWEST ID Badge #:________________  Expiration Date:______________

SSN:______________________

# Date completed test: ___/___/___

# Name of Service Supplier: _______________________________

# Current supervisor: _________________________________________

# Address and e-mail: ________________________________________

# Area of work (State):_____________________________

# Years of experience:__________________________

Have you ever worked in a Qwest Central Office:   yes_[   ]_  no_[   ]___

# Qwest Representative space only.

- Number missed________ Number of incorrect answers________  Number of incorrect references__________

- Which test numbers had incorrect answers______________________________________________________________

- Which test numbers had incorrect references____________________________________________________________

# Qwest Instructions For TP77350 Issue M Test

The following test is an open book test.  Everyone should have a copy of Technical Publication 77350 (Telecommunications Equipment Engineering, Installation And Removal Guidelines) before starting this test.

There are two (2) parts for every question.  Not only will you have to provide the correct answer but you will have to identify where the correct answer is stated within the Qwest installation guidelines (TP 77350).

# SAMPLE QUESTION

All connections made over solder or on terminals with solder connections shall be soldered.

- True

- False

# Answer ___A___ (correct answer is a)

# Chapter ___7___ paragraph__7.1.1__ (The answer can be found in chapter 7 paragraph 7.1.1)

If you come up with a different chapter and/or paragraph than what is called out on the test answer sheet, then that answer will be researched in order to determine if that is an alternate answer that should be included in the test answer sheet.

This will not be a pass/fail type of test, as everyone will be required to get a 100% on this test. In the event that you miss one or more questions (either you have the wrong answer or you have referenced the wrong chapter/paragraph on TP77350) then you will be required to retake only that portion of the test that you have erred on. If you still miss a question or more, than again you will retake only the portion that you have wrong, until you have achieved 100% on the test.  Once you have achieved 100% compliance, you will receive a certificate and your training records will be updated to include this accomplishment.

Note: If you are a supplier representative (installer) then your manager will be notified of the successful completion of this test and your training records will be handled by your company.

Remember the whole objective is to ensure that you are completely familiar with the Qwest Technical Publication 77350.

# GENERAL REQUIREMENTS

- Cell phones are ok to use while in a Central Office.

A.  True

B. False

Answer    	 	Chapter	        			Paragraph

- Safety glasses must be worn only when in or entering in the power room.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- If a service supplier disagrees with findings on an audit, who does the supplier appeal to?

- Anyone listening

- Quality Auditor

- Supplier’s Manager

- Central Office Manager

Answer    	 	Chapter	        			Paragraph

- An appeal must be made within 5 calendar days of receiving an audit.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- A Level 4 – Tech must have only a minimum of 6 years experience.

- True

- False

Answer    	 	Chapter	        			Paragraph

- If there are environmental concerns in any facility, when should service suppliers adjust or disable any HVAC, Humidity Control or Building Alarm System?

- Immediately

- Never

- After contacting a Qwest building representative

- None of the above

Answer    	 	Chapter	        			Paragraph

- Qwest is responsible to provide methods of handling products to prevent damage or deterioration.

- True

- False

Answer    	 	Chapter	        			Paragraph

- No network element shall be turned up for service without the equipment alarms wired and tested.

- True

- False

Answer    	 	Chapter	        			Paragraph

- The installer shall be required to run all alarm cables, perform standard continuity, power verifications and designate label per chap…

- 8

- 6

- 4

- none of the above

Answer    	 	Chapter	        			Paragraph

ASSEMBLY & IRONWORK

- A power cable rack located with in the power room area for battery stands must be set a minimum of

from the floor to the top of the rack.

- 4 feet

- 6 feet

- 7 feet

- 8 feet

Answer    	 	Chapter	        			Paragraph

- Is it necessary to locate additional brackets to add protection for cables at crossing points where cables break off the racks?

- Never

- Maybe

- Always

Answer    	 	Chapter	        			Paragraph

- In all earthquake zones, framing, battery stands & equipment must be at least 6 inches away from exterior, interior walls or columns.

- True

- False

Answer    	 	Chapter	        			Paragraph

- Under what circumstances will a service supplier cut or modify floor anchors?

- None

- Emergency

- Where ever necessary

- After Central Office approval

Answer    	 	Chapter	        			Paragraph

CABLE HOLES

- You must be 3M fire stopped trained and certified in order to complete proper firestopping.

- True

- False

Answer    	 	Chapter	        			Paragraph

- The approved firestopping cable hole label is		.

- RG  47-0132

- RG  47-0133

- RG  47-033

- RG  470130

Answer    	 	Chapter	        			Paragraph

- Qwest requires all wall penetrations be provided with what type of flange?

- Plastic

- None

- Metal

- Depends on the situation

Answer    	 	Chapter	        			Paragraph

- The spacing between each wall fastening bolt is 			.

- 3 inches

- 4 inches

- 5 inches

- 6 inches

Answer    	 	Chapter	        			Paragraph

CABLING

- Cables shall be run directly from point to point with only a “maintenance loop” of stack stored on the cable rack which should not exceed how many feet?

- 2 feet

- 4 feet

- 6 feet

- doesn’t matter

Answer    	 	Chapter	        			Paragraph

- What two items within power room location only, may be secured directly to a cable rack with a No. 9 cord?

- 750 power cables

- Battery & battery return cables

- Power alarms and monitoring leads

- None of the above

Answer    	 	Chapter	        			Paragraph

- Fiber cables are bundled together by wrapping the fiber cable group with sheet fiber paper and loosely securing with No. 1 cable.

- True

- False

Answer    	 	Chapter	        			Paragraph

- When sewing horizontal resting runs on dedicated power & switchboard cable racks, how many cables per stitch are used when the size of the wire is 400 kcmil or larger?

- 4

- 2

- 6

Answer    	 	Chapter	        			Paragraph

- Cable ties are approved for securing fiber optic cables in cable racks.

- True

- False

Answer    	 	Chapter	        			Paragraph

- Cable tie locking heads are permitted to have jagged cut ends as long as they don’t pose a safety hazard.

- True

- False

Answer    	 	Chapter	        			Paragraph

- Single fibers (1 – 12) can be loosely secured together provided they do not exceed how many square inches per stitch?

- 3

- 2

- 1

- none of the above

Answer    	 	Chapter	        			Paragraph

WIRING

- Under no circumstances shall spared wiring be coiled around in-service wiring.

- True

- False

Answer    	 	Chapter	        			Paragraph

- When cable wiring fans are under the transverse arm, what is required?

A.  Twine

B.  Stitching

C.  No rings

D.  Fanning rings

Answer    	 	Chapter	        			Paragraph

- Cable tags attached by the manufacturer that contain circuit identification info are cable tags and will be removed.

- True

- False

Answer    	 	Chapter	        			Paragraph

CONNECTING

- All single hole and two hole terminations for power and bonding/grounding shall require the use of what type of washer (except when double or locking are standard)?

- Lock washer

- Star lock washer

- Split ring lock washer

- Any of the above

Answer    	 	Chapter	        			Paragraph

- If necessary, what color heat shrinkable tubing may be used when insulation is required to protect the connector from shorting?

- Blue

- Beige

- Yellow

- Clear

Answer    	 	Chapter	        			Paragraph

- Compression crimps shall be permitted on solid wire of what size?

- 2/0 awg

- 16 gauge & smaller

- 12 gauge

- 1/0 awg

Answer    	 	Chapter	        			Paragraph

- A minimum of how many turns shall be made on all soldered, wrapped connections?

- 1

- 2

- 1 ¼

- 1 ½

Answer    	 	Chapter	        			Paragraph

- A minimum clearance of what shall be maintained between adjacent soldered connections?

- 1/32 of an inch

- ½ of an inch

- 1 inch

- ¼ if an inch

Answer    	 	Chapter	        			Paragraph

EQUIPMENT DESIGNATIONS

- When labeling the preferred method of color and background is what?

- Black letters on clear background

- Red letters on white background

- Black letters on white background

- None of t he above

Answer    	 	Chapter	        			Paragraph

- When should you use red labeling?

- Bay labels

- Caution notices

- Power boards

- Designation labels

Answer    	 	Chapter	        			Paragraph

- The procedure for numbering shelves within a bay, relay rack or equipment frame shall be consistent for all network elements utilized within Qwest.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- Marking drawings/records with all assignment changes is mandatory?

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- When designating battery stands, you must have the string name, voltage and

on the label.

A.  MOP number

B.  Cell number

C.  BVAPP number

D.  None of the above

Answer    	 	Chapter	        			Paragraph

- Battery stands associated with the back up of UPS systems must be clearly marked with “					“.

A.  GROUND WINDOW

B.  WARNING HAZARDOUS VOLTAGE

C.  DO NOT DISCONNECT

D.  INTEGRATED AREA

Answer    	 	Chapter	        			Paragraph

- Each rectifier must be designated with what?

A.  Group number

B.  Input voltage and fuse or breaker location

C.  Output voltages

D.  All of the above

Answer    	 	Chapter	        			Paragraph

POWER

- Typical power wiring color code for 120/240 volt is:

A.  Black – Red – Blue

B.  Brown – Orange – Yellow

C.  White or Gray

D.  Green

Answer    	 	Chapter	        			Paragraph

- Splices shall not be made in the open areas of frame bases, vertical cable ducts, or end guards unless they are approved for splicing.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- Metal flex conduit is approved to run in the power room.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- All work performed on or around energized circuits, must have what type of label.

A.  POWER CABLE ONLY

B.  WARNING HAZARDOUS MATERIAL

C.  LOCK OUT / TAG OUT

D.  None of the above

Answer    	 	Chapter	        			Paragraph

- All battery cables shall be secured together in….

A.  Fours

B.  Pairs

C.  Never

D.  Only when needed

Answer    	 	Chapter	        			Paragraph

- In power rooms, untinned wire will not be used where 			  are required.

A.  Fuses

B.  750 cable

C.  Class I flex

D.  Unfused leads

Answer    	 	Chapter	        			Paragraph

- Aluminum bus bars are ok for new installations.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- All bus bars must be a minimum of 		 from any metal objects.

A.  3 inches

B.  1 foot

C.  6 inches

D.  Doesn’t matter

Answer    	 	Chapter	        			Paragraph

- Battery return leads connected via a 2-hole compression lug to a battery return bus bar assembly should be stacked one on top of the other under the same mounting hardware to maximize the usage of the available mounting positions.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- What is the highest fuse amperage rating permitted for installation in a Battery Distribution Fuse Board (BDFB)?

A.  70A

B.  100A

C.  60A

Answer    	 	Chapter	        			Paragraph

- What is the largest size lead permitted for installation in a Battery Distribution Fuse Board (BDFB)?

A.  No. 2 AWG

B.  No. 350 MCM AWG

C.  No. 750 MCM AWG

Answer    	 	Chapter	        			Paragraph

STORAGE BATTERIES

- Qwest reps must be present for the following in order to proceed.

A.  Delivery of battery cells

B.  Cleaning of batteries

C.  Connecting of battery at bus bar

D.  A & C

Answer    	 	Chapter	        			Paragraph

- The following items are required to have on site when working with batteries.

A.  Goggles

B.  Eye Wash Kit

C.  Spill Kit

D.  All of the above

Answer    	 	Chapter	        			Paragraph

BONDING AND GROUNDING

- The grounding techpub is the 77350.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- Grounding conductors will should be run within cable racks or attached to the AC conduit.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- Frame ground connectors should be stacked one on top of the other under the same mounting hardware.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- Frame ground connectors should be stacked one on top of the other under the same mounting hardware.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

DOCUMENTATION

- It is ok to alter any form as a supplier sees fit to do so.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- The Job Packet must be kept in the Central Office, in the designated storage area of the location of work.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- The Job Packet Envelope must contain the following paperwork.

A.  DWP

B.  MOP

C.  Job Log

D.  All of the above

Answer    	 	Chapter	        			Paragraph

- A job log form is number 			.

A.  RG 47-001

B.  RG 40-0004

C.  RG 41-0046

D.  RG 42-0001

Answer    	 	Chapter	        			Paragraph

- A JIM stands for 					.

A.  Job installation material

B.  Job information memo

C.  Job in maintenance

D.  CO Manager

Answer    	 	Chapter	        			Paragraph

FORMS

- An RG 09-1031 is never needed in the Central Office.

A. True

B.  False

Answer    	 	Chapter	        			Paragraph

- Installation Job Logs are used to communicate daily job issues of relevance.

A. True

B.  False

Answer    	 	Chapter	        			Paragraph

- An Installation Completion Notice (ICN) should be turned in when?

A.  Job is complete

B.  Job is partially complete

C.  Job is turned over for service in advance

D.  Any of the above

Answer    	 	Chapter	        			Paragraph

- A MOP stands for what?

A.  Material on premise

B.  Modification of property

C.  Method of procedure

D.  Method of performance

Answer    	 	Chapter	        			Paragraph

- A detailed MOP needs to include a PNAR number.

A. True

B.  False

Answer    	 	Chapter	        			Paragraph

- An RG 47-0157 is the form for what?

A.  MOP

B.  Service Interruption

C.  COE

D.  JIM

Answer    	 	Chapter	        			Paragraph

- CLEC provisioning forms are used for communication between CLEC and service supplier.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

METHODS OF PROCEDURE

- A signed MOP must be posted where the work in going to begin prior to the work beginning.

A. True

B.  False

Answer    	 	Chapter	        			Paragraph

- The MOP header portion must be filled out to its entirety.

A. True

B.  False

Answer    	 	Chapter	        			Paragraph

- A MOP can be signed by….

A.  Anyone in the Central Office

B.  Qwest Central Office Operations Manager

C.  Qwest Quality Manager

D.  Any Central Office Technician

Answer    	 	Chapter	        			Paragraph

- If there is a service interruption, the service supplier must call…..

A.  Central Office Operations personnel

B.  UNICAL

C.  NROC

D.  All of the above

Answer    	 	Chapter	        			Paragraph

- PNAR number is for what purpose?

A.  Register work activities

B.  Control network activities

C.  Monitor outages

D.  All of the above

Answer    	 	Chapter	        			Paragraph

CLEC

- Qwest requires emergency access to all CLEC cages for _____  purposes.

A.  Quality

B.  Workmanship inspection procedures

C.  Fire, Life, Safety

Answer    	 	Chapter	        			Paragraph

- Qwest shall open and close all cable holes necessary to facilitate CLEC cabling.  The CLEC shall not open or close cable holes / penetrations.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- It is permissible for the CLEC to run AC power from Qwest AC panels (e.g., appliance outlets, etc.) for equipment testing purposes

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- CLEC equipment using the integrated ground plane within ______ feet of an ________ ground plane should be foreign-object grounded back to the ________  side of the CLEC ground window.

- 6, isolated, integrated

- 6, integrated, isolated

- 3, integrated, isolated

Answer    	 	Chapter	        			Paragraph

- When a CLEC terminates their business activities in Qwest facilities, it is referred to as:

A.  CLEC Hold

B.  CLEC Partial Hold

C.  CLEC Decommission

Answer    	 	Chapter	        			Paragraph

- For all CLEC provisioning and augmentation activities, the Service Supplier will complete the following form(s):

A.  RG 47-0130

B.  RG 47-0160

C.  RG 47-0131

Answer    	 	Chapter	        			Paragraph

DEFINITIONS

- A CAR is also known as a Corrective Action Report

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- DNA is the abbreviation for what?

A.  Chromosomes

B.  Did not apply

C.  Do not assign

D.  None of the above

Answer    	 	Chapter	        			Paragraph

- The abbreviation for ground is…

A.  G

B.  Green

C.  GRN

D.  GRD

Answer    	 	Chapter	        			Paragraph

- A PAR is also known as a quality audit.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph

- A SIN is also known as what?

A.  A bad act

B.  Supplier Notification Report

C.  Supplier Incident Notification

D.  None of the above

Answer    	 	Chapter	        			Paragraph

- The difference between the fiber optic jumper and patch cord is nothing but the name.

A.  True

B.  False

Answer    	 	Chapter	        			Paragraph