| 375 | J | 07/25/13 | 17 | Miscellaneous Publications | 17.3 | Added references to appropriate government CFR sections for engine compliance and UL requirements for Listing purposes, as well as ASME, API, Enersys, ITU, NACE, NETA, NIOSH, PEI, RUS, and TIA documents that were added as reference material in the main text of the document. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 374 | J | 07/25/13 | 17 | Telcordia Publications | 17.1 | Added GR-513 as a reference for the document | Level 4 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 373 | J | 07/25/13 | 15 | Test & Acceptance Forms | 15.3 | Modified the forms to be more generic in including all the types of NOCs from the legacy companies, and modified them to avoid the use of the terms CO and OSP where not necessary, since some legacy companies have different definitions of what those types of sites are. Removed requirement to use a meg-ohmmeter to test ground electrode fields (not always possible). Modified battery form to remove hydrometers but allow other types of temperature measurement at batteries besides thermometers. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 372 | J | 07/25/13 | 15 | Test & Acceptance Forms | 15.3 | Added many items based on combining the test and acceptance forms of the various Legacy companies. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 371 | J | 07/25/13 | 15 | Maintenance Window for Power | 15.2 | Genericized the text to try to avoid the use of the terms OSP and CO to make it more generic to all Legacy companies | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 370 | J | 07/25/13 | 15 | Maintenance Window for Power | 15.2 | Added guidelines for maintenance window hours that could potentially affect video circuits | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 369 | J | 07/25/13 | 14 | BDFBs | 14.3.11 | Added questions on return bars, dedicated primary power rack, and transitioning of overloaded BDFBs and miscellaneous fuse panels | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 368 | J | 07/25/13 | 14 | Standby Engine | 14.3.9 | Added question on engine grounding at the suggestion of a vendor | Level 1 | Additional informatioon | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 367 | J | 07/25/13 | 14 | AC Equipment | 14.3.8 | Added questions on transfer switches, inverters, UPS, and grounding | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 366 | J | 07/25/13 | 14 | Ring Plants | 14.3.7 | Added questions about ring plant type, capacity, grounding, and distribution at the suggestion of a detailed engineering vendor | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 365 | J | 07/25/13 | 14 | Converter Plants | 14.3.6 | Added questions about converter plant type, capacity, grounding, and distribution.at the suggestion of a detailed DC power engineering vendor | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 364 | J | 07/25/13 | 14 | Cable Racking | 14.3.3 | Added a question about fused and unfused cable rack at the suggestion of Detailed DC Power Engineering vendor | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 363 | J | 07/25/13 | 14 | Batteries | 14.3.2 | Added questions on battery stands at the suggestion of a detailed DC power engineering vendor | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 362 | J | 07/25/13 | 14 | Power Plants | 14.3.1 | Added questions on power plant types, Ethernet availability for PSMCs, and PDSCs at the suggestion of a detailed engineering vendor | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 361 | J | 07/25/13 | 14 | Detailed DC Power Engineering Audit | 14.2 | Renamed Chapter and Section to better describe the function of the chapter | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 360 | J | 07/25/13 | 13 | Power SNMP Traps | 13.6 | Added in Legacy CenturyTel Power SNMP Traps as part of making the document cover all CenturyLink companies | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 359 | J | 07/25/13 | 13 | Typical Power Alarm Points | 13.5 | Added typical power alarm tables for limited overhead bitstream point sites | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 358 | J | 07/25/13 | 13 | Typical Power Alarm Points | 13.5 | Genericized the alarms so that they fit all the Legacy companies that make up CenturyLink. Renumbered the sections in Chapter 13 due to the combination of multiple company alarming standards. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 357 | J | 07/25/13 | 13 | Power Alarm Thresholds | 13.4 | Added thresholds for battery float current rise, UPS battery ripple current, and battery impedance changes. Changed the acceptable range for charge current limiting to agree with CenturyLink standards. Added a reference to older CEMF cells. Totally redid the section in order to include the compromise thresholds agreed to in combining various company standards after the merger of companies. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 356 | J | 07/25/13 | 13 | Power Alarm Thresholds | 13.4 | Clarified threshold for BDFB current | Level 2 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 355 | J | 07/25/13 | 13 | Power Alarm Thresholds | 13.4 | Clarified which voltage tables apply to which battery types. Clarified the voltage threshold settings for converter plants and engine start batteries to better fit the lower voltage ranges. Clarified temperature compensation table and text. Modified uncontrolled engine room temperature threshold when engine is not running. Clarified that engine room low temperatures don’t have to be alarmed if there are block and battery heaters. Clarified alarming on plant shunts. Clarified battery string current imbalance to better fit test results. Renumbered the sections in Chapter 13 due to the combination of multiple company alarming standards. Genericized the text away from the use of CO and OSP where possible. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 354 | J | 07/25/13 | 13 | Alarm System Power Query Messages | 13.3 | Renumbered this section, and expanded its potential scope due to the combination of multiple internal company alarm standards. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 353 | J | 07/25/13 | 13 | Power Alarms for NMA | 13.2 | Combined sections 13.2 and the old 13.3, and added several new tables and rows to existing tables due to the combination of multiple internal company alarm standards | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 352 | J | 07/25/13 | 13 | Power Alarms for NMA | 13.2 | Removed AIDs and Condition Types that are no longer used | Level 1 | Removal | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 351 | J | 07/25/13 | 13 | Power Alarms – General | 13.1 | Genericized the section so that the chapter covers power alarms of all types from all the Legacy companies that now make up CenturyLink | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 350 | J | 07/25/13 | 13 | Power Alarm Messages and Thresholds | 13 | Changed the chapter title to reflect the fact that the section covers IP/SNMP in addition to TL1 messages | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 349 | J | 07/25/13 | 11 | Power Ped Technical Requirements | 11.3 | Clarified that an extra load center beyond the power pedestal is not necessary | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 348 | J | 07/25/13 | 11 | Power Pedestal Materials | 11.2 | Added information on unmetered service, and how it shouldn’t generally be used. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 347 | J | 07/25/13 | 11 | Power Pedestals – General | 11.1 | Avoided the use of the terms CO and OSP where possible due to differing meanings in legacy companies | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 346 | J | 07/25/13 | 11 | Power Pedestals – General | 11.1 | Added information on the preference for separate power pedestals, rather than power peds mounted to the RT | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 345 | J | 07/25/13 | 10 | Ring Plant Troubles | 10.4 | Added a maximum transfer interval for a ring generator based on RUS standards for switches | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 344 | J | 07/25/13 | 10 | Ring Plant Technical Requirements | 10.2 | Modified the upper input voltage range for ring plants to comply with RUS switching standards, and allowed 25 and 30 Hz ringing in special circumstances | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 343 | J | 07/25/13 | 10 | Ring Plant Technical Requirements | 10.2 | Added information on the types of power factors that could be expected in ringing loads, and the maximum allowable voltage and frequency variations. Also added temperature range compliance. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 342 | J | 07/25/13 | 9 | Fuse Sources | 9.6 | Excluded CLECs from fuse coordination rules | Level 3 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 341 | J | 07/25/13 | 9 | Fuse Sources | 9.6 | Changed normal maximum CenturyLink-owned BDFB fusing going forward back to 100 Amps due to what is commercially available from vendors. Made it desirable not to exceed 40% on any one side of a BDFB feeder, to normalize standards between all CenturyLink companies. | Level 2 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 340 | J | 07/25/13 | 9 | Fuse Sources | 9.6 | Removed the use of a List 1 drain estimating method for CenturyLink-owned equipment because that equipment is lab-tested, so there is no longer a need to estimate. | Level 4 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 339 | J | 07/25/13 | 9 | Fuse Sources | 9.6 | Clarified BDFB fuse position installation and numbering order. Moved the BDFB return bus higher in Figures 9-9 and 9-10 to allow for better cable access. Clarified that external return bars and limits on fuse/breaker sizing only apply to full-bay BDFBs for cable congestion reasons. Clarified that 50% rule applies to all A/B panels. Clarified that fuse coordination does not apply to 1-to-1 relationships between upstream and downstream protectors. Genericized away from use of the terms CO and OSP. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 338 | J | 07/25/13 | 9 | Protectors | 9.5 | Established a recommended maximum for protector sizing, but exempted CLECs from this requirement | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 337 | J | 07/25/13 | 9 | Protectors | 9.5 | Reduced company mvpc for lead-acid to 1 standard | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 336 | J | 07/25/13 | 9 | Cabling and Bus Bar | 9.4 | Provided standards for running DC leads outside of buildings, and allowed red and black power wiring for legacy RUS offices. Required multiple cables in the same main primary run to have the same circular mils, in keeping with the NEC, and in order to harmonize company standards. | Level 3 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 335 | J | 07/25/13 | 9 | Cabling and Bus Bar | 9.4 | Clarify conflict between Tech Pubs on 70 A-protected feeds and types of cable rack for them. Provided more definition around DLC cable. Softened requirement to tracer mark hard-rubber RHH/RHW. Included NNS requirement to not allow very small cables on power cable racks, and allowed segregation of power cable on switchboard racks in very small sites, as part of our multi-company standards harmonization. Genericized away from the use of the terms CO and OSP. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 334 | J | 07/25/13 | 9 | Equipment Loads | 9.2 | Clarified unfused flooded battery cable sizing to battery term bars, and cable sizing from batteries to plant when there is no MTB/chandelier arrangement. Made the text non-CO and OSP specific where it didn’t need to be. | Level 1 | Clarifications | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 333 | J | 07/25/13 | 9 | Equipment Loads | 9.2 | Clarified to which type of batteries listed MVPC applies, and combined company voltage drop and MVPC standards, Clarified that voltage drop standards do not apply to CLECs once power is handed off to them. | Level 2 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 332 | J | 07/25/13 | 9 | Equipment Loads | 9.2 | Added information on voltage drop from converter plants, and added ampacity tables from Tech Pub 77350 and other sources. Also, added the unwritten Qwest rule (but written for Legacy CTL) to feed A/B equipment out of the same BDFB bay. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 332 | J | 07/25/13 | 9 | Equipment Loads | 9.2 | Clarified which current to use in the voltage drop formula | Level 3 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 331 | J | 07/25/13 | 8 | Power Alarms in Sites w/o a PSMC | 8.7 | Added alarms based on combination of multiple company standards into the new CenturyLink | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 330 | J | 07/25/13 | 8 | Battery Monitors for UPS or small sites | 8.6.3 | Clarified that additional temperature probes are not usually necessary when battery temperature is being monitored for temperature compensation, clarified battery disconnect information, and added internal battery impedance monitoring. Clarified that CTs can be used to monitor AC ripple current in UPS, and that for UPS sites with a battery monitor, this section can also apply to engine start batteries. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 329 | J | 07/25/13 | 8 | Small Site Power Monitors | 8.6 | Revised the title and some text so that the section covers both small PSMCs and battery monitors (including UPS battery monitors) | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 328 | J | 07/25/13 | 8 | Energy Management | 8.5 | Clarified that Energy Management is only required for ferroresonant rectifiers | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 327 | J | 07/25/13 | 8 | Alarms | 8.3 | Added text to clarify backup alarms are only for PSMCs that are alarm-reporting, and allowed for SNMP communication | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 326 | J | 07/25/13 | 8 | AC Power Points | 8.2.9 | Added Ground Fault Detection as a required alarm for larger AC systems required to have it by Code and CenturyLink standard practice. Added information on monitoring AC voltage and current for sites with multiple transfer switches. Added information about proper protected feeds for the AC fail relay. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 325 | J | 07/25/13 | 8 | AC Power Points | 8.2.9 | Changed the should to a shall on fusing (or breaker protection) for AC fail relays | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 324 | J | 07/25/13 | 8 | Engine & Transfer Switch Points | 8.2.8 | Added single-phase lockout as a required alarm where the transfer switch is equipped with this feature, and added Day Tank Low Fuel as required when not combined into Fuel System Trouble. Also added Engine Fail to Parallel alarm for paralleled systems | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 323 | J | 07/25/13 | 8 | UPS Alarm Points | 8.2.7 | Added UPS Battery on Discharge alarm as part of combining company power alarm standards, and added an EPO alarm | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 322 | J | 07/25/13 | 8 | Inverter Points | 8.2.5 | Added “Bypass not available” as a required major alarm when a bypass exists, and the application is critical, due to the combining of company standards | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 321 | J | 07/25/13 | 8 | Battery Monitoring Points | 8.2.3 | Added binary points for smart batteries and battery monitoring systems, added Hall Effect devices for monitoring float current, mentioned differential temperature measurements and temperature compensation for VRLA batteries, and provided for the monitoring of internal battery impedance. Clarified battery disconnect breaker information. Added CTs to monitor AC ripple current for UPS systems. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 320 | J | 07/25/13 | 8 | Rectifier/Controller | 8.2.2 | Added information requiring PSMCs that double as the controller to be capable of energy management | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 319 | J | 07/25/13 | 8 | DC Plant Monitoring Points | 8.2.1 | Added and rearranged obvious binary power alarm points that were somehow missing from this section. Added inverter feeder current as an optional point to harmonize with national network standards internally | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 318 | J | 07/25/13 | 8 | General PSMCs and Battery Monitoring | 8.1 | Clarified that AC-powered alarm devices are OK for use with UPS or inverters. Also clsrified when PSMCs need to be capable of TL1. Clarified that PSMCs in sites with EPOs should generally be connected on the hot side of the disconnect to permit an alarm to report that the EPO has operated. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 317 | J | 07/25/13 | 8 | General PSMCs and Battery Monitoring | 8.1 | Added information on IP links for PSMCs and battery monitors, and SNMP OSMINE testing. Banned wireless communication of monitoring devices in most sites. Required super-user passwords to be changed and reported. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 316 | J | 07/25/13 | 8 | PSMCs and Battery Monitors | 8 | Renamed the Chapter to include battery monitors | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 315 | J | 07/25/13 | 7 | Portable Engine Connections | 7.19 | Modified the text so that the terms OSP and CO weren’t used in order to accommodate differing meanings of them | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 314 | J | 07/25/13 | 7 | Portable Engine Connections | 7.19 | Added IEC 60309 type devices from legacy CenturyLink and genericized the drawings to not be manufacturer specific. Also added information on maximum cord length for portable gensets less than 15 kW, and added labeling info for portable genset site-mounted receptacles. Added information on tap boxes for larger sites served by portables. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 313 | J | 07/25/13 | 7 | Portable Engine Trailers | 7.18 | Added a requirement to put adapter cordsets so that the portable can be connected to various plug/receptacle types. Added the NEC requirement that 30 A single-phase receptacles on the genset must be GFCI-protected. Added information to this section about considering multi-phase multi-voltage portable gensets. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 312 | J | 07/25/13 | 7 | Engine Safety | 7.16 | Added requirements for engine and fuel tank signage required by Codes | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 311 | J | 07/25/13 | 7 | Cooling Systems | 7.15 | Added requirements around minimum sizing of an airflow system, and minimum size of outdoor engine requiring a coolant sight glass. Added a preference for water-cooled vs. air-cooled engines. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 310 | J | 07/25/13 | 7 | Cooling Systems | 7.15 | Clarified that on-set radiator fans need to be shrouded with a duct flange for safety reasons, and that louvers open and and close with the engine start/stop signaling. Modified the text so that the section also applies to non-COs.. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 309 | J | 07/25/13 | 7 | Cold Starting Aids | 7.13 | Clarified preferred type of heater hose valves | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 308 | J | 07/25/13 | 7 | Exhaust Systems | 7.11 | Added information on the flange for dry exhaust manifolds, and on minimum distance of exhaust termination from fuel tank openings. Added a suggestion to place the muffler close to the engine to reduce unwanted carbon deposits. Added information on when a water drain for an exhaust system may be considered. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 307 | J | 07/25/13 | 7 | Fuel and Oil Systems | 7.10 | Clarified minimum fuel tank sizing for harder to get to areas, and clarified that not all engines have fuel separators. Clarified the minimum length of flexible fuel piping at the engine connection, and when day tanks or high-lift pumps are required due to distance and height of the engine from the main tank. Clarified the routing of the crank case breather tube. Clarified the usage of LP and gasoline fuels. Compromised on minimum tank size based on combining various internal policies of the legacy companies combining into the new CenturyLink. Clarified that day tanks must have two supply lines for reliability purposes, and removed requirement for a return line from day tank to main tank, since it is not really required. Clarified the requirements for catwalks on engines with base-tanks. Clarified maximum fill requirements for diesel and propane tanks. Maqde the text non-CO-specific. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 306 | J | 07/25/13 | 7 | Fuel and Oil Systems | 7.10 | Guidelines on preferred tank types. Allowed an anti-siphon valve as an alternative to a solenoid valve in sites w/o day tanks, and added guidance on bypasses for solenoids and anti-siphon valves. Added guidelines for exhaust system inspection schedule sources. Added placement restrictions of fuel tanks near water sources. Added a minimum tank design overfill capacity. Added requirements for natural gas/LPG piping. Required engine oil coolers for new diesel engines in keeping with legacy CenturyLink requirements. Added requirements for a drainpipe on engines without an easily accessible pan. Added cathodic protection information for direct-buried tanks. Allowed Essential-AC-driven fuel pumps in certain circumstances. Allowed double-walled fuel piping, and recommended instances when fuel piping should be buried. Required fire valves on pressurized indoor diesel fuel lines going forward in most instances. Added cathodic protection references and additional recommendations for direct-buried steel tanks. Added information on the rare use of return line fuel pumps. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 305 | J | 07/25/13 | 7 | Alarms/Shutdowns | 7.9 | Allowed an anti-siphon valve as an alternative to a solenoid valve in sites without day tanks. Provided further information on overspeed typical set points. Added undervoltage as a required shutdown feature (already generally available on almost all engine-alternators) in order to harmonize company standards. Added information on maximum turbine overspeed. Added guidance on proper settings for ground fault detection. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 304 | J | 07/25/13 | 7 | Engine Control and Transfer System Requirements | 7.5 | Added information about disconnecting from commercial AC on overvoltage and overfrequency conditions, and bonding on-set control cabinets. Added a requirement for a lamp test feature. Required new transfer gear to be microprocessor or PLC-controlled. Added a minimum time delay for engine start (5 seconds) on loss of AC and retransfer (15 min). Required locks on outdoor cabinets. Added a preference to not put transfer switches outdoors. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 303 | J | 07/25/13 | 7 | Transfer System Requirements | 7.5 | Clarified that automatic engine run timers going forward generally only need to be monthly timers. Clarified the standards for engine control cabinets. Clarified the open transition with both transfer breaker systems and transfer switches. Clarified minimum engine loaded and unloaded (cooldown) run times. Modified the text so that non-CO buildings are included.. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 302 | J | 07/25/13 | 7 | Alternator Requirements | 7.4 | Removed old alternator overload testing requirement because it was wrong, and the correct one was previously mentioned in the section | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 301 | J | 07/25/13 | 7 | Alternator Requirements | 7.4 | Added alternator insulation life requirements from CenturyLink standards. Added estimated altitude derating when a chart doesn’t exist | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 300 | J | 07/25/13 | 7 | Engine Sizing/Ratings | 7.3 | Added soft start requirements for VFDs to avoid the need to oversize engines. Added more information and a preference of options for permanent and portable load banks vs. no load banks. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 299 | J | 07/25/13 | 7 | Building AC System | 7.2 | Modified the text so that the section covers non-COs too | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 298 | J | 07/25/13 | 7 | General Engine | 7.1 | Modified the text so that the chapter covers non-COs too | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 297 | J | 07/25/13 | 7 | General Engine | 7.1 | Added requirements from legacy CenturyLink regarding engine enclosure pads. Added information on comparmetizing engines, and bollards for both above-ground diesel and propane tanks. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 296 | J | 07/25/13 | 6 | UPS Alarming and Control | 6.4 | Referred the reader to Chapter 8 for information on optional UPS battery monitoring | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 295 | J | 07/25/13 | 6 | UPS Technical Requirements | 6.3 | Clarified that breaker coordination only applies to our equipment, and clarified the DC voltage that may be present in medium and large UPS. Clarified when shunt-trip UPS feeder and output breakers are required. | Level 2 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 294 | J | 07/25/13 | 6 | UPS Definitions | 6.2 | Noted the new trend for minimum UPS battery backup sizing of 5 minutes (instead of the traditional 15), and provided guidance on additional reserve times and actual reserve times vs. design reserve times. Also noted special battery backup requirements for UPS serving more critical Network circuits, especially in COs | Level 1 | Additonal information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 293 | J | 07/25/13 | 5 | Inverter Technical Requirements | 5.5 | Clarified that n+1 inverters must be able to retain synchronization on loss of the shelf/bay controller, and that not all inverters are separately derived | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 292 | J | 07/25/13 | 5 | Inverter Selection | 5.2 | Provided guidance on choosing a DC plant vs. an inverter plant vs. a UPS | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 291 | J | 07/25/13 | 5 | Inverters – General | 5.1 | Expanded on the use of CenturyLink inverters in Collocation, that was already covered in Chapter 1 | Level 2 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 290 | J | 07/25/13 | 5 | Inverters – General | 5.1 | Removed emergency egress lighting as a valid load for DC plant inverters to keep AHJs out of the DC plant equipment because it is “not covered” by the NEC. Genericized away from the use of the terms CO and OSP to be more inclusive of all types of sites in various legacy companies. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 289 | J | 07/25/13 | 4 | Line-Powering | 4.4 | Added a new section on Line Powering | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 288 | J | 07/25/13 | 4 | Conveters - Technical Requirements | 4.3 | Added PANI MGB as a potential grounding point for a separately-derived (isolated) converter plant output | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 287 | J | 07/25/13 | 4 | Converters – General | 4.1 | Added already publicly-available information on CenturyLink collocation policies around the placement of DC-DC converters by CLECs in CenturyLink-owned space | Level 2 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 286 | J | 07/25/13 | 3 | Battery Disconnects | 3.10 | Clarified that MVPC listed only appliesto lead-acid batteries. Removed requirement to have battery cable ampacity exceed battery disconnect size because it is a disconnect and not a protector. This brings all internal companies on par with National long haul Network standards. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 285 | J | 07/25/13 | 3 | Battery Disconnects | 3.10 | Added information on battery disconnects for Li-ion batteries (built-in), and typical sizes for VRLA long-duration batteries and UPS. Required battery disconnects for flooded batteries when there is no unfused cable rack. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 284 | J | 07/25/13 | 3 | Battery Stands | 3.9.3 | Removed paragraph about heat shrink on battery cables because it is better-covered in Tech Pub 77350 | Level 1 | Removal | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 283 | J | 07/25/13 | 3 | Battery Stands | 3.9.3 | Clarified wording around connector coatings for direction connection to battery posts. Clarified exceptions to 2-string VRLA rule. Clarified the use of different types of flooded battery spill containment systems. Clarified labeling of strings going forward and for very large plants.. Clarified that when Li-ion or other front access batteries need side (such as for fold-out handles) or rear access, then spacing must be provided. Clarified an exception on anchors for when the wide-washer/head anchors won’t fit on certain battery stands.. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 282 | J | 07/25/13 | 3 | Battery Stands | 3.9.3 | Added a Listing requirement for permanently placed spill containment pillows, and added information about the Fire Code requirements to seal spill containment area floors. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 281 | J | 07/25/13 | 3 | Round Cell Stands | 3.9.2 | Clarified that round cell stands are no longer made | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 280 | J | 07/25/13 | 3 | Battery Sizing | 3.8 | Provided a sizing MVPC for Ni-Cd OSP batteries, and provided minimum backup times for certain types of DSL and video loads. Provided an average age-derating factor for battery sizing. Brought all 24-cell string lead-acid mvpc standards for all internal companies to a common 1.86 (and corrected 23-cell mvpc to 1.94). Added approvals needed to parallel Li-ion strings with lead-acid strings. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 279 | J | 07/25/13 | 3 | Battery Types | 3.6 | Removed LMP batteries because they are being removed from CemturyLink’s Network and are no longer available for telecom applications | Level 2 | Correction | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 278 | J | 07/25/13 | 3 | Battery Types | 3.6 | Clarified that there are limited circumstances where VRLAs may be placed in parallel with flooded batteries, and clarified the maximum rectifier voltage needed for VRLAs. Clarified when VRLAs can be used in COs. Clarified that round cells are no longer made. Clarified that VRLA boost charging can be done in PV applications. Removed verbiage around dual VRLA strings since it is now better covered in 3.9.3. Genericized away from the use of the terms OSP and CO where possible. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 277 | J | 07/25/13 | 3 | Battery Types | 3.6 | Added the use of Ni-Cd batteries in OSP applications, and allowed the use of lead-selenium designs in standby applications. Added information on storage life of battery types. | Level 2 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 276 | J | 07/25/13 | 3 | Battery Types | 3.6 | Added requirements of battery manufacturers to ship new flooded strings as voltage-matched sets manufactured in the same time frame. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 275 | J | 07/25/13 | 3 | Battery Configurations | 3.5 | Added requirements for battery room signage required by Codes | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 274 | J | 07/25/13 | 3 | Battery Configurations | 3.5 | Clarified that low-gravity VRLA strings may be paralleled with flooded battery strings. Strengthened requirements to ensure VRLA strings aren’t improperly paralleled with flooded | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 273 | J | 07/25/13 | 3 | Battery Recharge Characteristics | 3.4 | Noted changed rectifier sizing rule of 125% (primarily for VRLAs), and that equalize/boost charging is generally only for single cells | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 272 | J | 07/25/13 | 3 | Battery Discharge | 3.3 | Softened language to discourage rather than prohibit adjacent placement of first and last string cells due to common Legacy CenturyLink practices | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 271 | J | 07/25/13 | 3 | General Battery Requirements | 3.2 | Clarified backup rules for DSL | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 270 | J | 07/25/13 | 2 | Conventional Controller | 2.6 | Added HVSD as a required alarm for the conventional controller | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 269 | J | 07/25/13 | 2 | Conventional Controller | 2.6 | Clarified that only 1 master controller is allowed per DC plant. Clarified that generic major and minors must be available. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 268 | J | 07/25/13 | 2 | New PBD Panel and Protector Numbering | 2.5 | Genericized it so that the requirements could include non-Legacy Q systems | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 267 | J | 07/25/13 | 2 | List 1/2 Example | 2.4.1 | Added a whole new subsection to show how to properly apply List 1 and List 2 drains | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 266 | J | 07/25/13 | 2 | Engineering Guidelines | 2.4 | Clarified when less than 120% can be used for rectifier sizing due to some new rectifiers not capable of that. Changed 30% recharge excess capacity rule to 25% due to harmonization of merged company standards. Genericized cable rack pileup issues to all larger sites (not just COs). | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 265 | J | 07/25/13 | 2 | Engineering Guidelines | 2.4 | Noted the 10% additional battery load rule to account for the average of constant power loads during discharge. | Level 1 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 264 | J | 07/25/13 | 2 | Engineering Guidelines | 2.4 | Clarified the conditions under which List 2 drain is calculated, and that List 2 only applies to protector sizing (List 1 times 125% is used for voltage drop in some cases) | Level 2 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 263 | J | 07/25/13 | 2 | Engineering Guidelines | 2.4 | Added examples of how to calculate List 1 drain for non-POTS equipment | Level 2 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 262 | J | 07/25/13 | 2 | Rectifiers | 2.3 | Clarified that a default float voltage of 2.17 to 2.23 V/cell applies only to flooded and low-gravity VRLA lead-acid batteries. Clarified (in order to agree with other sections) that when CO-type site rectifiers are not individually fed, that the “spare” rectifier calculation is modified. Clarified that remote ground windows for busbar plants are only needed in certain offices. Clarified that remote sense only applies to DC plants with MTBs. Genericized away from the use of the terms OSP and CO where possible. Modified the discussion on sequencing to mostly refer them to section 8.5 for the valid reasons to do so. Clarified that locking AC plugs are not required if equipment is run to a rack-mount PDU in the same bay. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 261 | J | 07/25/13 | 2 | Rectifiers | 2.3 | Added information from other public documents specifying CenturyLink collocation policies for rectifiers, batteries, and fuel cells, so that all power standards (including collocation) were in the same document | Level 2 | Additional information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 260 | J | 07/25/13 | 2 | General DC Power Plant Requirements | 2.2 | Modified the alternate battery type in Figure 2-2 from LMP to Ni-Cd. Relaxed the requirement prohibiting LVBDs going forward to allow them in Customer Premises. Clarified the use of conventional and monitoring types of DC plant controllers. Clarified typical load shed times. Genericized away from the use of the terms OSP and CO. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 259 | J | 07/25/13 | 1 | Generic Alarming Requirements | 1.7 | Clarified that ring terminals are not required for alarm connections, and that miscellaneous fusel panels may not always be alarmed | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 258 | J | 07/25/13 | 1 | NEBS Requirements | 1.6 | Clarified that NEBS requirements only apply in NEBS-compliant equipment space (not to engine rooms for example). Clarified that Listing requirements for connectors and wire apply to all sites (not just COs) | Level 3 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 257 | J | 07/25/13 | 1 | Generic Technical Requirements | 1.5 | Clarified that fuse coordination only applies to CenturyLink equipment, and does not apply when the relationship between upstream and downstream is 1-to-1. | Level 3 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 256 | J | 07/25/13 | 1 | Generic Technical Requirements | 1.5 | Clarified the types of power connectors that can be used for lifeline telephony supporting equipment. Removed requirement for fuse color-coding because that only applies to certain types of fuses. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 255 | J | 07/25/13 | 1 | AC Surge Suppression | 1.4.1 | Provided a new section for AC surge suppression devices. Clarified TVSS sizing for radio and IOF fiber regen sites, and the maximum breakdown voltages for 208, 240, and 480 VAC entrances. Clarified the preferred placement, connection, and distance maximum for a TVSS. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 254 | J | 07/25/13 | 1 | AC Requirements | 1.4 | Clarified requirements that rectifiers fed from secondary panels must be dedicated PDSCs, but allowed exceptions for small sites. Clarified that copper wire for AC circuits is only absolutely required in CenturyLink-owned sites. Genericized where possible the use of the terms CO and OSP due to their differing meanings in Legacy companies.. | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 253 | J | 07/25/13 | 1 | AC Requirements | 1.4 | Added information from other public documents specifying CenturyLink collocation policies on AC power, so that all power standards (including collocation) were in the same document. | Level 2 | Additional Information | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 252 | J | 07/25/13 | 1 | Requirement Applicability | 1.3 | Noted that a CLEC ICA supersedes this document | Level 2 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 251 | J | 07/25/13 | 1 | General | 1.1 | Modified the equipment lower operating voltage range slightly to agree with Telcordia. Included RUS standards compliance to a certain degree; and included ±190 VDC as a bulk-powering voltage option | Level 1 | Clarification | NETW.TECH.07.10.13.F.11291.Final_TP_77385_Iss_J |
| 250 | I | 9/25/09 | 1 | Reason for Issuance | 1.2 | Added a new “Reason for Reissue” Section | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 249 | I | 9/25/09 | 17 | Ordering Info. | 17.4 | Added ordering information for various standards bodies | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 248 | I | 9/25/09 | 17 | Ordering Info. | 17.4 | Revised ordering procedure for Qwest employees to match new process | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 247 | I | 9/25/09 | 17 | Publications | 17.3 | Added numerous ANSI, ASTM, IEEE, NEMA, OSHA, and UL publications | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 246 | I | 9/25/09 | 17 | Telcordia Pubs | 17.1 | Added numerous Telcordia publications and their respective descriptions | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 245 | I | 9/25/09 | 16 | Definitions | 16 | Added numerous Acronyms and Definitions | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 244 | I | 9/25/09 | 15 | Forms | 15.3 | Added check for confined space labeling requirements | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 243 | I | 9/25/09 | 15 | Forms | 15.3 | Added battery re-connect threshold information | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 242 | I | 9/25/09 | 15 | Forms | 15.3 | Added bulleted point for a check of rectifier sizing based on load | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 241 | I | 9/25/09 | 15 | Forms | 15.3 | Added rectifiers to be included with the meter accuracy check | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 240 | I | 9/25/09 | 15 | Forms | 15.3 | Added 14th point for earthquake check | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 239 | I | 9/25/09 | 15 | Forms | 15.3 | Added spill containment and battery disconnect verification | Level 1 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 238 | I | 9/25/09 | 15 | Forms | 15.3 | Added check to verify if temperature compensation is operational | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 237 | I | 9/25/09 | 15 | Forms | 15.3 | Asked for the number of spare fuses/positions to be reported to engineering | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 236 | I | 9/25/09 | 15 | Mtce. Window Guidelines for Power | 15.2 | Added section allowing maintenance window to be extended for OSP | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 235 | I | 9/25/09 | 15 | Mtce. Window Guidelines for Power | 15.2 | Added section detailing maintenance window hours for DSL | Level 3 | Changes that have a moderate effect on CLEC operation procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 234 | I | 9/25/09 | 14 | BDFBs | 14.3.11 | Required a SAR and embargo to correct a BDFB overload condition | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 233 | I | 9/25/09 | 14 | Tables | 14 | Added BDFB capacity table reference to match new table addition in chapter | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 232 | I | 9/25/09 | 13 | Power SNMP | 13.7 | Added entire new section 13.7 for power SNMP traps for DSL and Ethernet | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 231 | I | 9/25/09 | 13 | Analog Setpoints | 13.5 | Added engine room, engine battery, & coolant temperature thresholds to table | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 230 | I | 9/25/09 | 13 | Analog Setpoints | 13.5 | Added table 9 for Lithium based battery alarm specifications | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 229 | I | 9/25/09 | 13 | Analog Setpoints | 13.5 | Adjusted some alarm threshold values to harmonize combined company standards. Clarified the use of equalize/boost charging. | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 228 | I | 9/25/09 | 13 | Analog Setpoints | 13.5 | Added 53.8 to 55.2 Voltage range for this table to specify included batteries | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 227 | I | 9/25/09 | 13 | Analog Setpoints | 13.5 | Added section discouraging the use of LVDs | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 226 | I | 9/25/09 | 13 | Analog Setpoints | 13.5 | Added section explaining temperature compensation’s effects on VRLAs | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 225 | I | 9/25/09 | 13 | Analog Setpoints | 13.5 | Added section explaining VRLA batteries’ pilot cell variations on new installs | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 224 | I | 9/25/09 | 13 | Analog Setpoints | 13.5 | Clarified Major vs. Minor alarm standards based on the type of points | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 223 | I | 9/25/09 | 13 | Reduced TL1 | 13.3 | Added additional SUB-AIDs/AIDs | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 222 | I | 9/25/09 | 13 | AIDs and Condition Types for Power Alarms | 13.2 | Clarification updates were made within this section | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 221 | I | 9/25/09 | 13 | General | 13.1 | Added NNS information | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 220 | I | 9/25/09 | 12 | Task | 12.2 | Explained the proper use and reasoning for engine enclosure lighting | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 219 | I | 9/25/09 | 12 | Task | 12.2 | Explained proper use/sizing of ground wire based on -48 V return conductor | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 218 | I | 9/25/09 | 12 | Task | 12.2 | Updated minimum wire size to reflect current standards | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 217 | I | 9/25/09 | 12 | Emergency | 12.1 | Added 2 other sources of lighting | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 216 | I | 9/25/09 | 11 | Materials | 11.3 | Clarification updates were made within this section | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 215 | I | 9/25/09 | 11 | Materials | 11.2 | Explained that some utilities require an external disconnect | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 214 | I | 9/25/09 | 11 | Materials | 11.2 | Explained meter socket acceptability and local requirements for electricians | Level2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 213 | I | 9/25/09 | 11 | General | 11.1 | Clarification, additions and grammatical updates were made through out the section | Level2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 212 | I | 9/25/09 | 10 | Ringing Plant alarms and Troubles | 10.4 | Clarification updates were made within the section | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 211 | I | 9/25/09 | 10 | Distribution | 10.3 | Clarification, additions and grammatical updates were made through out the section | Level2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 210 | I | 9/25/09 | 10 | Ringing and Tone Systems Technical Requirements | 10.2 | Clarification, additions and grammatical updates were made through out the section | Level2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 209 | I | 9/25/09 | 9 | Bus Bar Labeling and Layouts | 9.7 | Clarification, additions and grammatical updates were made through out the section | Level2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 208 | I | 9/25/09 | 9 | Fuse Sources | 9.6 | Added requirement so that blown fuses will not have a residual Voltage | Level2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 207 | I | 9/25/09 | 9 | Fuse Sources | 9.6 | Added BDCBB to BDFB requirements | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 206 | I | 9/25/09 | 9 | Fuse Sources | 9.6 | Required equipment fed from a 50 A DC fuse or larger to have a 2 hole lug | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 205 | I | 9/25/09 | 9 | Fuse Sources | 9.6 | Added section of acceptable ways to power equipment from 2 sources | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 204 | I | 9/25/09 | 9 | Fuse Sources | 9.6 | Removed signage requirements | Level 2 | Correction | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 203 | I | 9/25/09 | 9 | Fuse Sources | 9.6 | Changed must to should when installing fuse positions from bottom up | Level 2 | Correction | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 202 | I | 9/25/09 | 9 | Fuse Sources | 9.6 | Removed equalize ground section for BDFBs due to newer equipment | Level 2 | Correction | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 201 | I | 9/25/09 | 9 | Fuse Sources | 9.6 | Allowed BDFB distributions to higher/lower floors | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 200 | I | 9/25/09 | 9 | Fuse Sources | 9.6 | Added guarding requirements for unused BDCBB breaker positions | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 199 | I | 9/25/09 | 9 | Fuse Sources | 9.6 | Added max fuse/breaker sizing requirements to 150 A DC for BDFB/BDCBBs | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 198 | I | 9/25/09 | 9 | Protectors and Cable Sizing | 9.5 | Clarification, additions and grammatical updates were made through out the section | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 197 | I | 9/25/09 | 9 | Cabling and Bus Bar | 9.4 | Added section explaining suggested placement of battery return bus | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 196 | I | 9/25/09 | 9 | Cabling and Bus Bar | 9.4 | Added LNS requirements for power cable brackets for smaller cables | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 195 | I | 9/25/09 | 9 | Cabling and Bus Bar | 9.4 | Added red DC colored cable usage requirements | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 194 | I | 9/25/09 | 9 | Power Plant Distribution Characteristics | 9.3 | Added information for Qwest equipment (not applicable to CLECs) for distribution fuses and circuit breakers | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 193 | I | 9/25/09 | 9 | Equipment Loads | 9.2 | Added a paragraph for miscellaneous fuse panel voltage drop exemption. This only impacts Qwest Figure 9-3 - Clarified information about the chandelier and added the word “unfused” to battery cables | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 192 | I | 9/25/09 | 9 | Equipment Loads | 9.2 | Added BDCBB (Battery Distribution Circuit Breaker Boards) to BDFB so it will read BDFB/BDCBB multiple times within this section | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 191 | I | 9/25/09 | 9 | Equipment Loads | 9.2 | Provided clarification for the formula for calculating Voltage drop and added specifications for National Network Standards (NNS) | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 190 | I | 9/25/09 | 8 | batteries | 8.6.3 | Clarified and added info for Analog points (String float current added) and clarified info for Binary Points | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 189 | I | 9/25/09 | 8 | Requirements of a PSMC for Con-fined Locations | 8.6 | Required PSMC-CL to have backup MJ, MN, and watchdog backup alarms run | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 188 | I | 9/25/09 | 8 | Energy Manage | 8.5 | Added notation explaining rare uses of sequencing | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 187 | I | 9/25/09 | 8 | Standby Engines and Transfer Systems | 8.2.8 | Added overfill as a required alarm if not part of the fuel system trouble | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 186 | I | 9/25/09 | 8 | Standby Engines and Transfer Systems | 8.2.8 | Added engine supplying load alarm as an optional alarm | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 185 | I | 9/25/09 | 8 | UPS | 8.2.7 | Added UPS Fail as a required alarm if available | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 184 | I | 9/25/09 | 8 | Residual Ringing Plants | 8.2.6 | Clarified Binary Points | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 183 | I | 9/25/09 | 8 | Inverters | 8.2.5 | Clarified Binary Points | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 182 | I | 9/25/09 | 8 | Converter Plants | 8.2.4 and 8.2.5 | Moved Binary Points info from 8.2.5 to 8.2.4 and deleted section | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 181 | I | 9/25/09 | 8 | Batteries | 8.2.3 | Clarified the Binary Points | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 180 | I | 9/25/09 | 8 | Batteries | 8.2.3 | Clarified the monitoring requirements for newer types of batteries and require that the room temp sensor is placed away from heating/cooling equipment | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 179 | I | 9/25/09 | 8 | Rectifiers | 8.2.2 | Renamed section from Chargers to Rectifiers and clarified Rectifier Fail (RFA) | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 178 | I | 9/25/09 | 8 | Primary Power Plant | 8.2.1 | Added a Note for Binary Points regarding the power plant major and minor alarms | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 177 | I | 9/25/09 | 8 | Primary Power Plant | 8.2.1 | Clarified Analog Points | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 176 | I | 9/25/09 | 8 | General | 8.1 | Recommended tagging of alarm wires | Level1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 175 | I | 9/25/09 | 8 | General | 8.1 | Added the option for engineers to waive BDFB monitoring requirements | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 174 | I | 9/25/09 | 8 | General | 8.1 | Added special password requirement to monitors that allow plant control | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 173 | I | 9/25/09 | 8 | General | 8.1 | Clarified remote access requirements for PSMCs | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 172 | I | 9/25/09 | 8 | General | 8.1 | Added notation recommending a separate PSMC for every plant | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 171 | I | 9/25/09 | 7 | Portables | 7.18 | Added towing lights requirements | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 170 | I | 9/25/09 | 7 | Safety | 7.16 | Re-worded Rotating Parts section for readability | Level 0 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 169 | I | 9/25/09 | 7 | Safety | 7.16 | Clarified engine insulation and guarding requirements | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 168 | I | 9/25/09 | 7 | Safety | 7.16 | Added warning label requirements and exhaust temperature suggestions | Level 1 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 167 | I | 9/25/09 | 7 | Cooling System | 7.15 | Added section explaining requirements and suggestions for louvers | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 166 | I | 9/25/09 | 7 | Cooling System | 7.15 | Added sight glass requirement for radiators on engines above 800 kW | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 165 | I | 9/25/09 | 7 | Cooling System | 7.15 | Added requirement that remote radiators be grounded to the OPGP | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 164 | I | 9/25/09 | 7 | Cooling System | 7.15 | Modified the high temperature threshold to 50C/122F | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 163 | I | 9/25/09 | 7 | Cold Starting Aids | 7.13 | Added notes on half-powered heaters and circulation pumps | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 162 | I | 9/25/09 | 7 | Cold Starting Aids | 7.13 | Added valve addition recommendation to aid in changing heaters and hoses | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 161 | I | 9/25/09 | 7 | Starting Systems | 7.12 | Added temperature compensation recommendation for chargers | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 160 | I | 9/25/09 | 7 | Exhaust System Requirements | 7.11 | Added 7 foot rule to exhaust insulation requirement | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 159 | I | 9/25/09 | 7 | Exhaust System Requirements | 7.11 | Added walk-in enclosure exception to pipe guarding rules | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 158 | I | 9/25/09 | 7 | Fuel/Lube Systems | 7.10 | Added details regarding the venting of oil vapors | Level 1 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 157 | I | 9/25/09 | 7 | Fuel/Lube Systems | 7.10 | Added fuel cup and fuel path details | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 156 | I | 9/25/09 | 7 | Fuel/Lube Systems | 7.10 | Added details regarding fire marshal requirements for a fuel shutoff valve | Level 3 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 155 | I | 9/25/09 | 7 | Fuel/Lube Systems | 7.10 | Added anti siphon valve in the feed line as a requirement | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 154 | I | 9/25/09 | 7 | Fuel/Lube Systems | 7.10 | Added details to fuel solenoid-operated valve section | Level2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 153 | I | 9/25/09 | 7 | Fuel/Lube Systems | 7.10 | Added section to require fuel lines to extend halfway down the engine | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 152 | I | 9/25/09 | 7 | Fuel/Lube Systems | 7.10 | Added catwalk requirement to engines more than 7' high with a belly tank | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 151 | I | 9/25/09 | 7 | Fuel/Lube Systems | 7.10 | Added to the section describing fuel tank sizing | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 150 | I | 9/25/09 | 7 | Fuel/Lube Systems | 7.10 | Added double wall requirement for direct buried tanks | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 149 | I | 9/25/09 | 7 | Fuel/Lube Systems | 7.10 | Added acceptable fuels section for clarity of approved backup generators | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 148 | I | 9/25/09 | 7 | Alarms and Shutdowns | 7.9 | Clarified preliminary high coolant temperature alarm requirements | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 147 | I | 9/25/09 | 7 | Additional Paralleling Requirements | 7.8 | Updated the section name to better provide the content of the section. The new name is Additional Paralleling Requirements | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 146 | I | 9/25/09 | 7 | Voltage and Frequency Regulation | 7.7 | Clarified when load on an engine-alternator is increased in 25% steps | Level 2 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 145 | I | 9/25/09 | 7 | Additional Engine Requirements | 7.6 | Updated the section name to better provide the content of the section. The new name is Additional Engine Requirements | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 144 | I | 9/25/09 | 7 | Control Cabinet and Transfer System Requirements | 7.5 | Added section explaining single phase lockout requirements if AC is lost | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 143 | I | 9/25/09 | 7 | Control Cabinet and Transfer System Requirements | 7.5 | Added recommendation for control system to be close to the generator | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 142 | I | 9/25/09 | 7 | Control Cabinet and Transfer System Requirements | 7.5 | Added control cabinet as acceptable mounting place for gauges | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 141 | I | 9/25/09 | 7 | Control Cabinet and Transfer System Requirements | 7.5 | Added “shall” to require circuit wiring to be stranded | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 140 | I | 9/25/09 | 7 | Alternator Technical Requirements | 7.4 | Added additional alternator requirements | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 139 | I | 9/25/09 | 7 | Sizing & Ratings | 7.3 | Added details explaining need for sequencing or lead/lag control | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 138 | I | 9/25/09 | 7 | Site AC Power Systems | 7.2 | Added section describing basic alternator sizing requirements for engines | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 137 | I | 9/25/09 | 7 | Site AC Power Systems | 7.2 | Required AC disconnect to be nearby to the engine room | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 136 | I | 9/25/09 | 7 | General | 7.1 | Required age limits on and inspections of engines before reuse | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 135 | I | 9/25/09 | 7 | General | 7.1 | Added detail on Qwest requiring a factory representative going to the job site for the initial start up of an engine-alternator | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 134 | I | 9/25/09 | 7 | General | 7.1 | Added detail on P.E.s and floor loading for engines and earthquake zones | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 133 | I | 9/25/09 | 7 | General | 7.1 | Required single line diagrams to be on site when a system is added/updated | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 132 | I | 9/25/09 | 7 | General | 7.1 | Added section describing up-sizing the alternators as an option to changeout | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 131 | I | 9/25/09 | 7 | General | 7.1 | Added details regarding grounding system for engines | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 130 | I | 9/25/09 | 7 | General | 7.1 | Added section to dissuade the use of emergency in lieu of standby due to NEC | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 129 | I | 9/25/09 | 6 | Alarming and Control | 6.4 | Clarified alarming and microprocessor section | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 128 | I | 9/25/09 | 6 | Technical Requirements | 6.3 | Required UPS VRLA batteries to be high rate | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 127 | I | 9/25/09 | 6 | Technical Requirements | 6.3 | Added output voltage requirement and included specs for output distortion | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 126 | I | 9/25/09 | 6 | Technical Requirements | 6.3 | Explained the usage of EPO switches and requirements surrounding them | Level 1 | clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 125 | I | 9/25/09 | 6 | Technical Requirements | 6.3 | Added battery component and cable running requirements to this section | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 124 | I | 9/25/09 | 6 | Definition of Terms | 6.2 | Added information on flywheels, and line-interactive and on/off-line UPS | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 123 | I | 9/25/09 | 6 | Definition of Terms | 6.2 | Removed charger section and replaced with double conversion section | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 122 | I | 9/25/09 | 5 | Technical Requirements DC/AC Power Supplies | 5.5 | Added NEC requirements for grounding and ground reference of inverters | Level 2 | Additional Info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 121 | I | 9/25/09 | 5 | General | 5.1 | Added details explaining the use of a static transfer switch | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 120 | I | 9/25/09 | 4 | Technical | 4.3 | Changed requirement for individual converter feeds and explained spares | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 119 | I | 9/25/09 | 4 | Alarm Features | 4.2 | Clarified minimum alarming considerations | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 118 | I | 9/25/09 | 4 | Converters (DC/DC) - General | 4.1 | Removed discharge fuse capacity section | Level 1 | Correction | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 117 | I | 9/25/09 | 3 | Battery Disconnect | 3.10 | Added new point explaining how to figure voltage drop | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 116 | I | 9/25/09 | 3 | Battery Disconnect | 3.10 | Added information on ampacity and voltage drop when using a disconnect | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 115 | I | 9/25/09 | 3 | Battery Disconnect | 3.10 | Added information on quick disconnects and shunt trip disconnects | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 114 | I | 9/25/09 | 3 | Battery “Stand” Installation | 3.9.3 | Clarified paragraph on Battery bus bars over flooded battery stands | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 113 | I | 9/25/09 | 3 | Battery “Stand” Installation | 3.9.3 | Clarified minimum height requirements | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 112 | I | 9/25/09 | 3 | Battery “Stand” Installation | 3.9.3 | Added additional information for spill containment and room construction | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 111 | I | 9/25/09 | 3 | Battery “Stand” Installation | 3.9.3 | Added spill neutralization requirements for large and small flooded cells | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 110 | I | 9/25/09 | 3 | Battery “Stand” Installation | 3.9.3 | Clarified heat shrink section for proper heat shrink guidelines on battery lugs | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 109 | I | 9/25/09 | 3 | Battery “Stand” Installation | 3.9.3 | Added new section for spacing of VRLA and Li-based cells | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 108 | I | 9/25/09 | 3 | Round Cell Stands | 3.9.2 | Added details for round cell stands | Level 1 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 107 | I | 9/25/09 | 3 | Metal Stands, Trays & Compartments/Boxes | 3.9.1 | Added new section explaining grounding for trays/stands | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 106 | I | 9/25/09 | 3 | Metal Stands, Trays & Compartments/Boxes | 3.9.1 | Added paragraph explaining requirements for trays in outdoor RT cabinets. | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 105 | I | 9/25/09 | 3 | Sizing | 3.8 | Added new section on Lithium batteries in -48 V plants in COs | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 104 | I | 9/25/09 | 3 | Sizing | 3.8 | Added new section on special sizing rules with Lithium-based batteries | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 103 | I | 9/25/09 | 3 | Sizing | 3.8 | Added minimum end cell voltage requirements for all types of sites | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 102 | I | 9/25/09 | 3 | Sizing | 3.8 | Added clarification to required reserve time of radio sites and solar fed sites | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 101 | I | 9/25/09 | 3 | Sizing | 3.8 | Added details about, DSL, CPE and wireless backhaul service reserve time | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 100 | I | 9/25/09 | 3 | Sizing | 3.8 | Added new details and requirements for minimum reserve times for batteries | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 99 | I | 9/25/09 | 3 | Selection | 3.7 | Added new section on use of battery heater pads for RT cabinets | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 98 | I | 9/25/09 | 3 | Battery Types | 3.6 | Added entire new section on super capacitors | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 97 | I | 9/25/09 | 3 | Battery Types | 3.6 | Added and clarified information on Li battery charge voltages | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 96 | I | 9/25/09 | 3 | Battery Types | 3.6 | Added section on Nickel-Metal Hydride batteries | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 95 | I | 9/25/09 | 3 | Battery Types | 3.6 | Added information on cycling/solar batteries in low temperature environments | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 94 | I | 9/25/09 | 3 | Battery Types | 3.6 | Added new section to explain minimum cell requirements | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 93 | I | 9/25/09 | 3 | Battery Types | 3.6 | Added wording on VRLA use in LNS | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 92 | I | 9/25/09 | 3 | Battery Types | 3.6 | Clarified lead antimony float current information | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 91 | I | 9/25/09 | 3 | Battery Configurations | 3.5 | Added additional information on mixing cells and specific gravities in a string | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 90 | I | 9/25/09 | 3 | Battery Recharge Characteristics | 3.4 | Replaced entire section on VRLA with more details on all plate types | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 89 | I | 9/25/09 | 3 | Battery Recharge Characteristics | 3.4 | Added Li battery information about rectifier sizing | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 88 | I | 9/25/09 | 3 | Battery Discharge Characteristics | 3.3 | Explained coup de fouet differences | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 87 | I | 9/25/09 | 3 | Battery Discharge Characteristics | 3.3 | Included new types of batteries and formulas for figuring out end cell voltages | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 86 | I | 9/25/09 | 3 | General Description | 3.2 | Added detail for battery manufacturing standards and design lifetimes | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 85 | I | 9/25/09 | 3 | General Description | 3.2 | Added detail for UPS reserve requirements and lifeline backup | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 84 | I | 9/25/09 | 3 | General Description | 3.2 | Added detail about non-requirements of back up power for DSL | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 83 | I | 9/25/09 | 2 | Conventional Controller | 2.6 | New requirement to parallel PSMC and plant controller MJ/MN alarms | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 82 | I | 9/25/09 | 2 | Conventional Controller | 2.6 | Added 100 A plants as the minimum size requiring remote monitors | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 81 | I | 9/25/09 | 2 | Engineering Guidelines | 2.4 | A new paragraph detailing cable sizing and voltage drop for rectifier shelves | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 80 | I | 9/25/09 | 2 | Engineering Guidelines | 2.4 | Additional information for various rectifier sizes | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 79 | I | 9/25/09 | 2 | Engineering Guidelines | 2.4 | Added more information regarding n+1 redundancy in all Qwest sites | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 78 | I | 9/25/09 | 2 | Charging Eqpt (Rectifiers) and Their Controller | 2.3 | Added customer waiver for lack of TVSS provision to Qwest | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 77 | I | 9/25/09 | 2 | Charging Eqpt (Rectifiers) and Their Controller | 2.3 | Added details for rectifiers larger than 65 A | Level 2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 76 | I | 9/25/09 | 2 | Charging Eqpt (Rectifiers) and Their Controller | 2.3 | Clarified DC ripple noise | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 75 | I | 9/25/09 | 2 | Charging Eqpt (Rectifiers) and Their Controller | 2.3 | Changed recommended threshold values for rectifier current limit | Level 2 | Correction and additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 74 | I | 9/25/09 | 2 | Charging Eqpt (Rectifiers) and Their Controller | 2.3 | Added ENERGY MANAGEMENT information for the proper plant operation, rectifiers/charging equipment features | Level 2 | Correction and additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 73 | I | 9/25/09 | 2 | Charging Eqpt (Rectifiers) and Their Controller | 2.3 | Removed first sentence of the first paragraph regarding when charging equipment is added to an existing power plant | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 72 | I | 9/25/09 | 2 | DC Power Plant and Rectifiers | 2.2 | Clarified LVD usage with DSL (load shedding) | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 71 | I | 9/25/09 | 2 | DC Power Plant and Rectifiers | 2.2 | Added RHH and XHHW as acceptable wire types, as well as TFFN | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 70 | I | 9/25/09 | 2 | DC Power Plant and Rectifiers | 2.2 | Explained charge current limit of the rectifiers to prevent runaway/overload and clarified the principle components of the power distribution plant | Level 1 | Correction and clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 69 | I | 9/25/09 | 1 | Generic Alarming Requirements | 1.7 | Removed requirement for plant indicators to blink because it was unnecessary and updated alarm output for the office alarm system | Level 1 | Correction and clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 68 | I | 9/25/09 | 1 | Generic Alarming Requirements | 1.7 | Covered appropriate use of mid-trip vs electro-magnetic breakers | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 67 | I | 9/25/09 | 1 | NEBS Requirements | 1.6 | Clarified NEBS requirements, certification and compliance | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 66 | I | 9/25/09 | 1 | Generic Technical Requirements | 1.5 | Clarified generic technical requirements | Level1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 65 | I | 9/25/09 | 1 | AC Requirements | 1.4 | Added additional TVSS requirements | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 64 | I | 9/25/09 | 1 | AC Requirements | 1.4 | Added an exception on conduit set screws to agree with other Tech Pubs | Level2 | Additional info. | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 63 | I | 9/25/09 | 1 | AC Requirements | 1.4 | Clarified what types of conduit can and cannot be used to feed rectifiers | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 62 | I | 9/25/09 | 1 | AC Requirements | 1.4 | Clarified PDSC Requirements | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 61 | I | 9/25/09 | 1 | AC Requirements | 1.4 | Added exceptions for the use of THHN/THWN wire in DC circuits | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 60 | I | 9/25/09 | 1 | AC Requirements | 1.4 | Added examples of essential and non-essential loads | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 59 | I | 9/25/09 | 1 | General | 1.1 | Added Voltage ranges and changed the existing one to agree with Telcordia | Level 1 | Clarification | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 58 | I | 9/25/09 |  | Comments page |  | Updated address and e-mail on where to send comments | Level 2 | Correction | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 57 | I | 9/25/09 |  | Notice page |  | The use of the words “relevant or “applicable” were removed within this document unless specifically agreed upon via the Ad Hoc meetings from 4-24-09 through 7-29-09. Updated the origin of Technical Publication 77385, specifically referring to this as “Technical Publication” as opposed to “document”; this reference is continued through out the Technical Publication as clarification is appropriate | Level 3 | Changes that have a moderate effect on CLEC operating procedures | NETW.TECH.08.31.09.F.06855.TechPub_77385_Iss_I |
| 56 | G | 4/15/02 | A | Alarms | 12 | Moved all Annex material of previous issue to chapter 12 | Level 2 | Correction | Unavailable |
| 55 | G | 4/15/02 | 15 | References | 15 | Renumbered this from previous issue, where it was chapter 14 | Level 1 | Correction | Unavailable |
| 54 | G | 4/15/02 | 14 | Definitions | 14 | Renumbered this from previous issue, where it was chapter 13 | Level 1 | Correction | Unavailable |
| 53 | G | 4/15/02 | 13 | Test & Acceptance | 13 | Added a new chapter with test and acceptance forms for power equipment | Level 1 | Additional info. | Unavailable |
| 52 | G | 4/15/02 | 12 | Analog Thresholds | 12.5 | Added engine start batteries to the same table as converter thresholds | Level 1 | Additional info. | Unavailable |
| 51 | G | 4/15/02 | 12 | Analog Thresholds | 12.5 | Clarified setting of HVSD between rectifiers and plant controller | Level 1 | Clarification | Unavailable |
| 50 | G | 4/15/02 | 12 | Analog Thresholds | 12.5 | Added information on being careful about equalizing VRLA batteries | Level 1 | Additional info. | Unavailable |
| 49 | G | 4/15/02 | 11 | Lighting | 11 | Added information on labeling of inverter-powered lighting | Level 1 | Additional info. | Unavailable |
| 48 | G | 4/15/02 | 11 | Lighting | 11 | Added information on color codes for DC lighting wiring | Level 1 | Additional info. | Unavailable |
| 47 | G | 4/15/02 | 11 | Lighting | 11 | Clarified a potential problem with right-hand-thread DC bulbs | Level 1 | Clarification | Unavailable |
| 46 | G | 4/15/02 | 10 | General | 10.1 | Added EUSERC requirements for certain areas for Power Peds | Level 1 | Additional info. | Unavailable |
| 45 | G | 4/15/02 | 8 | Bus Bars | 8.7 | Added new section on busbar labeling and layout | Level 1 | Additional info. | Unavailable |
| 44 | G | 4/15/02 | 8 | Fuse Sources | 8.6 | Added figures showing placement of BDFB return bars | Level 1 | Additional info. | Unavailable |
| 43 | G | 4/15/02 | 8 | Fuse Sources | 8.6 | Added text describing placement of BDFB return bars | Level 1 | Additional info. | Unavailable |
| 42 | G | 4/15/02 | 8 | Cable Sizing | 8.5 | Clarified the ampacity to be used for BDFB feeders | Level 1 | Clarification | Unavailable |
| 41 | G | 4/15/02 | 8 | Cable Sizing | 8.5 | Clarified load to be used for battery cable voltage drop sizing | Level 1 | Clarification | Unavailable |
| 40 | G | 4/15/02 | 8 | Bus Bars | 8.4 | Added reference for clearance of bus bars | Level 1 | Clarification | Unavailable |
| 39 | G | 4/15/02 | 8 | Cabling | 8.4 | Added references for cable requirements and ampacity | Level 1 | Additional info. | Unavailable |
| 38 | G | 4/15/02 | 8 | Equipment Loads | 8.2 | Clarified battery cable ampacity sizing when a disconnect exists | Level 1 | Additional info. | Unavailable |
| 37 | G | 4/15/02 | 8 | Equipment Loads | 8.2 | Added information on fuse sizing for leads out of misc fuse panels | Level 1 | Additional info. | Unavailable |
| 36 | G | 4/15/02 | 8 | Equipment Loads | 8.2 | Added information on protector sizing for feeds to misc fuse panels | Level 1 | Additional info. | Unavailable |
| 35 | G | 4/15/02 | 8 | Equipment Loads | 8.2 | Added voltage drop standards for switch PDFs | Level 1 | Additional info. | Unavailable |
| 34 | G | 4/15/02 | 7 | No PSMC | 7.7 | Added a new section on what to monitor when there is no PSMC | Level 1 | Additional info. | Unavailable |
| 33 | G | 4/15/02 | 7 | Batteries | 7.2.3 | Added monitoring of battery string disconnects | Level 1 | Additional info. | Unavailable |
| 32 | G | 4/15/02 | 7 | Batteries | 7.2.3 | Clarified the number of battery cell temperatures to be monitored | Level 1 | Clarification | Unavailable |
| 31 | G | 4/15/02 | 7 | Batteries | 7.2.3 | Clarified methods of monitoring string current | Level 1 | Clarification | Unavailable |
| 30 | G | 4/15/02 | 7 | Monitor Points | 7.2 | Clarified when optional points may be monitored | Level 1 | Clarification | Unavailable |
| 29 | G | 4/15/02 | 7 | General | 7.1 | Clarified that modems and PADs must be DC-powered | Level 1 | Clarification | Unavailable |
| 28 | G | 4/15/02 | 7 | General | 7.1 | Recommendation for PSMC in each DC plant | Level 1 | Additional info. | Unavailable |
| 27 | G | 4/15/02 | 6 | Acoustic Noise | 6.14 | Allowed an exception on engine enclosure fans at high altitude | Level 1 | Additional info. | Unavailable |
| 26 | G | 4/15/02 | 6 | Fuel Systems | 6.10 | Defined the amount of solids that could be in the fuel stream | Level 1 | Clarification | Unavailable |
| 25 | G | 4/15/02 | 6 | Fuel Systems | 6.10 | Clarified the use of day tanks | Level 1 | Clarification | Unavailable |
| 24 | G | 4/15/02 | 6 | Frequency | 6.7 | Added a definition of “steady-state” | Level 1 | Additional info. | Unavailable |
| 23 | G | 4/15/02 | 6 | Engine Control | 6.5 | Added requirement for a test switch | Level 1 | Additional info. | Unavailable |
| 22 | G | 4/15/02 | 4 | Technical | 4.5 | Added information on separately-derived source grounding of inverters | Level 1 | Additional info. | Unavailable |
| 21 | G | 4/15/02 | 4 | General | 4.1 | Added task and stumble lighting as items that could be inverter-powered | Level 1 | Additional info. | Unavailable |
| 20 | G | 4/15/02 | 4 | General | 4.1 | Clarified when AC-powered Network equipment needs an inverter | Level 1 | Clarification | Unavailable |
| 19 | G | 4/15/02 | 4 | General | 4.1 | Added information on when the maintenance bypass is not required | Level 1 | Additional info. | Unavailable |
| 18 | G | 4/15/02 | 4 | General | 4.1 | Clarification of the preferred operating mode for inverters | Level 1 | Clarification | Unavailable |
| 17 | G | 4/15/02 | 3 | Technical | 3.3 | Added information on separately-derived source grounding of converters | Level 1 | Additional info. | Unavailable |
| 16 | G | 4/15/02 | 2 | Engineering | 2.6 | Clarified that jacks must be provided to measure plant current w/o meter | Level 1 | Clarification | Unavailable |
| 15 | G | 4/15/02 | 2 | Battery Disconnect | 2.5 | Added a table for battery disconnect sizing | Level 1 | Additional info. | Unavailable |
| 14 | G | 4/15/02 | 2 | Battery Disconnect | 2.5 | Added a new section on battery disconnects | Level 1 | Additional info. | Unavailable |
| 13 | G | 4/15/02 | 2 | Batteries | 2.4 | Added information on the choosing of the pilot cell | Level 1 | Additional info. | Unavailable |
| 12 | G | 4/15/02 | 2 | Batteries | 2.4 | Referenced cable sizing for battery cables to Chapter 8 | Level 1 | Clarification | Unavailable |
| 11 | G | 4/15/02 | 2 | Batteries | 2.4 | Added information on separation of battery term bars | Level 1 | Additional info. | Unavailable |
| 10 | G | 4/15/02 | 2 | Batteries | 2.4 | Added information on conformance of battery rooms to the Fire Code | Level 1 | Additional info. | Unavailable |
| 9 | G | 4/15/02 | 2 | Batteries | 2.4 | Added requirements on re-use of batteries | Level 1 | Additional info. | Unavailable |
| 8 | G | 4/15/02 | 2 | Batteries | 2.4 | Added information on what to do to replace MD’d batteries | Level 1 | Additional info. | Unavailable |
| 7 | G | 4/15/02 | 2 | Batteries | 2.4 | Added information on string naming | Level 1 | Additional info. | Unavailable |
| 6 | G | 4/15/02 | 2 | Batteries | 2.4 | Clarified cell numbering requirements | Level 1 | Clarification | Unavailable |
| 5 | G | 4/15/02 | 1 | Alarms | 1.6 | Added information on where alarm leads can be run | Level 1 | Additional info. | Unavailable |
| 4 | G | 4/15/02 | 1 | NEBS | 1.5 | Added Listing requirement | Level 1 | Additional info. | Unavailable |
| 3 | G | 4/15/02 | 1 | NEBS | 1.5 | Clarified NEBS applicability for subsystems | Level 1 | Clarification | Unavailable |
| 2 | G | 4/15/02 | 1 | Technical | 1.4 | Added information on protector labeling | Level 1 | Additional info. | Unavailable |
| 1 | G | 4/15/02 | 1 | AC requirements | 1.3 | Clarified the use of AC wire types | Level 1 | Clarification | Unavailable |